## Slide 1: The Scope
Wireless Security Lab
  Attacker and Defender Nodes
  Send wireless signals from Defender node to server
  Website to control VMware ESXi server
OpenBTS (Base Transceiver Station)
  Implement using USRP
    Universal Software Radio Peripheral
  LabVIEW / GNURadio
  Phone Call, SMS

## Slide 2: Wireless Lab Topography

## Slide 3: Hardware Architecture Diagram

## Slide 4: Software Architecture Diagram

## Slide 5: Current Design
Software
  ESXi
  Operating Systems
  Website
Hardware
  LabVIEW
  GNURadio
  Asterisk
Requirements Engineering

## Slide 6: OpenBTS System Overview
MSC/VLR
Notes: Open BTS Architecture
Open BTS software architecture is an emulation of GSM 04.03. In uplink direction, data arriving from handsets to USRP is processed with Analog to Digital
Converter (ADC). Data is then packaged with TCP/IP headers with time stamp and transferred to the host CPU using Gigabit Ethernet interface. Open BTS
transceiver synchronizes the USRP with the GSM master clock and demodulates symbol vectors for each radio. TDM layer of the GSM stack demultiplexes each burst and passes on to FEC processor. Data Link Layer (L2) then accepts the corrected data and runs link layer, segmentation and retransmission (LAPDm) processor. Signaling and Connection Management of L3 determines the message protocol and calls the appropriate control function to deserialize the message and act on its content. These control-functions also communicate with the outside world via SIP and
other protocols.

## Slide 7: OpenBTS Implementation
USRP
  Receive/Transmit GSM signals
Asterisk
  Server
GNURadio
  Open-source software development toolkit
LabVIEW
  View signal output

## Slide 8: Technical Challenges
LabVIEW
Operating system compatibility
Security
Outdated environment
Exploring new technologies
  LAMP, ESX Shell, ESX API’s

## Slide 9: Testing Plan {Hardware}
USRP Testing
  Signal output verification
  Spectrum sweeping
Functional Verification Testing
  LabVIEW
    View capture signals.
  OpenBTS
    Assign a phone number to each registered handset.
    Allow a phone to call another one.
    Allow a phone to send SMS message to another one.

## Slide 10: Testing Plan {Software}
Front-end Website Testing
  Functional User Testing
Back-end Modules
  ESX Shell, ESX API’s
  Login System
  Class Creation
System Infrastructure Testing
System Integration Testing

## Slide 11: Website
Webserver Location:
  http://129.186.215.201
Our Website:
  http://seniord.ece.iastate.edu/dec1314/
George Amariucai’s Website:
  http://home.eng.iastate.edu/~gamari/
CprE 537 Website:
  http://home.eng.iastate.edu/~gamari/CprE537_S12/index.html

## Slide 12: Questions?

## Slide 13: Wireless Lab Implementation
VMware
  Backend Support
Kali Linux
  Attack Clients
Ubuntu Client
  Data Transmission Client
Webserver
  Interface to Launch Clients

## Slide 14: Virtualization Flowchart

## Slide 15: The GSM Network

## Slide 16: What is OpenBTS?
A software-based GSM access point.
It uses open-source UNIX application to present a GSM air interface to standard GSM handset devices.
In other word OpenBTS = GSM + VoIP